## Slide 1: Checkpoint #3 Obstacle Avoidance
Due : 11/20/2020

## Slide 2: Outline
CP 3 Supplies
Checkpoint #3 Assignment
Hardware Configuration
Introduce to GPIO of Raspberry Pi
Photo resistor sensor and Touch sensor
Checkpoint#2 Demo & grading

## Slide 3: CP 3 Supplies
1
COM
NC
NO
2

## Slide 4: Checkpoint #3 Assignment
The purpose of this checkpoint is to make sure you can control your robot to move in the arena. The mobile robot needs to detect an obstacle in front of it and take action to avoid the obstacle in order to continue its motion.
Further, your robot can find the puck. In this checkpoint, the puck is a ring of LED lights.

## Slide 5: Checkpoint #3 Grading Policy
Please start to arrange the space configuration of your robot, make sure every and each component such as circuit boards and sensors is settled firmly and stable on the chassis and all the robot functions will not be affected by wires. (15%)
Make sure that your robot can move freely. It means that you do not need to use keyboard to control it anymore. (20%)
Integrate a light sensor and two touch sensors to the robot and program your robot to find and move toward the puck (LED light). (30%)
The time to find the puck (in 90 sec). (35%)

## Slide 6: Checkpoint #3

## Slide 7: Hardware Configuration

## Slide 8: GPIO of Raspberry Pi
GPIO: General-Purpose Input/Output
Notes: A powerful feature of the Raspberry Pi is the row of GPIO which stands for general-purpose input/output,
The Raspberry Pi has two rows of GPIO pins along the top edge of the board.
Any of the GPIO pins can be designated (in software) as an input or output pin and used for a wide range of purposes.
Output pins are like switches that the Raspberry Pi can turn on or off (like turning on/off a LED light). But it can also send a signal to another device.
Input pins are like switches that you can turn on or off from the outside world (like a on/off light switch). But it can also be a data from a sensor, or a signal from another device.
And other GPIO pins can be used with a variety of alternative functions, some are available on all pins, others on specific pins.
We take PWM signal as example,
Software PWM available on all pins
Hardware PWM available on GPIO12, GPIO13, GPIO18, GPIO19

## Slide 9: Wiring Pi: GPIO interface library
WiringPi is an attempt to bring Arduino-wiring-like simplicity to the Raspberry Pi.
The goal is to have a single common platform and set of functions for accessing the Raspberry Pi GPIO across multiple languages.
Installation:
  C: $ gpio –v
  Python: $ sudo pip install wiringpi2
Reference: http://wiringpi.com/download-and-install/

## Slide 10: WiringPi’s Pin number
Prints a table of WiringPi’s Pin number on terminal.
$ gpio readall

## Slide 11: WiringPi’s Pin number
Website Reference: https://pinout.xyz/pinout/wiringpi

## Slide 12: Example Code
Sensor‘s pin is connected to Header pin 15 and the WiringPi pin is 3.
Include the Head file
#include <wiringPi.h>
Library setup function.
wiringPiSetup () ;
Setup pin mode
int sensor_pin = 3; //wiringpi’s pin
pinMode (sensor_pin, INPUT) ;
Read pin’s data
sensor_data = digitalRead(sensor_pin) ;

## Slide 13: Photo resistor sensor
Use Photo resistor sensor to detect the LED light.
connect to Pi3’s 5V.
GND connect to Pi3’s GND.
connect to GPIO Pin.
You can change the Variable Resistor to increase the sensitivity of the sensor. If the brightness is bright enough, will be 0.

## Slide 14: Touch sensor
Integrate touch sensors to avoid an obstacle and walls of the area.
COM
NC
NO

## Slide 15
Deadline
--------------------------------------------
Checkpoint#3 Demo : 11/20
Checkpoint #3 Report : 11/27

## Slide 16: CP #2 Demo Time
Group A 09:30 ~ 10:30 | Group B 10:30 ~ 11:30
Team 7 | Team 1
Team 8 | Team 2
Team 9 | Team 3
Team 10 | Team 4
Team 11 | Team 5
Team 12 | Team 6
Team 13 |